## Slide 1: PROCESS CONTROL AND ANALYSIS
LECTURE TWO

## Slide 2: Gain
The proportional action of a controller is generally called the proportional gain. This means that the controller moves proportional to the error
Where K = proportional gain
Many terms have been used to denote this action namely proportional gain, or simply gain, throttling band, sensitivity and or proportional band (PB).

## Slide 3: Proportional Band
The controller out-put of the proportional controller is expressed as:
The proportional gain, K, is often expressed in terms of another parameter called proportional band (PB).
The PB is the error required to move the FCE over its entire range.
It is expressed as a percentage of the total range of the measured variable:

## Slide 4
Practically the controller output is limited, either by own limitations or by the corresponding actuator.
If Umax and Umin are the minimum and maximum outputs of a controller.
The proportional band of the controller is then defined as:

## Slide 5
In the ideal case, a controller can have an unlimited output. The proportional band (PB) is then defined as:
This definition of proportional band is often used instead of the controller gain. The value is expressed in percent (%).

## Slide 6: Bandwidth
In computer networks, bandwidth means data transfer rate, the amount of data that can be carried from one point to another in a given time period (usually a second).
Network bandwidth is usually expressed in bits per second (bps);

## Slide 7
In control engineering, bandwidth is the range of frequencies, i.e., the difference between the highest and lowest-frequency signal components.
Like the signal frequency, bandwidth is measured in hertz (cycles per second).
This is the original definition of bandwidth.
Study question:
compare the meaning of bandwidth and proportional band

## Slide 8: Off-set
There is always an error to produce a controller output. This means that with proportional control only, there will always be a small offset between the set-point and the measured variable.
To remove this offset, an integral control is added.

## Slide 9: Integral Action
With integral action, the controller output is proportional to the amount of time the error is present.
Integral action eliminates offset from the proportional control.
It is also known as reset.

## Slide 10
Integral action gives the controller a large gain at low frequencies that results in eliminating offset.
However, integrals give information concerning the past. That is why integrals are always late or slow acting.
Integrals provide stability but have a tendency to get stuck in the past.
In most controllers the proportional and integral action are combined.

## Slide 11: Actuators
An actuator is a mechanism for turning energy into motion.
It is a component of a machine that is responsible for moving or controlling a mechanism or system, for example by opening or closing a valve; in simple terms, it is a "mover".
Actuators can be categorized by the energy source they require to generate motion.

## Slide 12
For example: Pneumatic actuators use compressed air to generate motion.
Hydraulic actuators use liquid to generate motion.
Electric actuators use an external power source, such as a battery, to generate motion.
Thermal actuators use a heat source to generate motion.
The data from energy source is generated and provided by sensors.

## Slide 13
An actuator requires a control signal and a source of energy.
The control signal is relatively low energy and may be electric voltage or current, pneumatic or hydraulic pressure, or even human power.
When the control signal is received, the actuator responds by converting the energy into mechanical motion.
The control system can be simple (a fixed mechanical or electronic system) or software-based (e.g., a printer driver, robot control system)

## Slide 14: Sensors
A sensor is a device that detects and responds to some type of input from the physical environment.
The specific input could be light, heat, motion, moisture, pressure, or any one of a great number of other environmental phenomena.
The output is generally a signal that is converted to human-readable display at the sensor location or transmitted electronically over a network for reading or further processing.

## Slide 15
In a mercury-based glass thermometer, the input is temperature.
The liquid contained expands and contracts in response, causing the level to be higher or lower on the marked gauge, which is human-readable.
Study question
What are the different types of sensor?

## Slide 16
Motion sensors in various systems including home security lights and automatic doors usually send out some type of energy, such as microwaves or light beams and detect when the flow of energy is interrupted by something moving in their paths.

## Slide 17
A photo sensor detects the presence of visible light, infrared and/or ultraviolet energy.
Applications of photo-sensors include: fiber optic systems; optical scanners; wireless LANs; automatic lighting controls; optical disk drives; optical memory chips and remote control devices

## Slide 18: Characteristics of sensors
A good sensor has the following characteristics:
It is sensitive to the measured property
It is insensitive to any other property likely to be encountered in its application, and
It does not influence the measured property.
Most sensors have a linear transfer function

## Slide 19
The sensitivity is the ratio between the output signal and measured property.
For example, if a sensor measures temperature and has a voltage output, the sensitivity is a constant with the units [V/K].
The sensitivity is the slope of the transfer function.

## Slide 20
Converting the sensor's electrical output (for example V) to the measured units (for example K) requires dividing the electrical output by the slope (or multiplying by its reciprocal).
In addition, an offset is frequently added or subtracted.

## Slide 21: Time Constant
This the time which represents the speed with which a particular system can respond to change, typically equal to the time taken for a specified parameter to vary by a factor of 1− 1/ e (approximately 0.6321).

## Slide 22
In physics and engineering, the time constant, is the parameter characterizing the response to a step input of a first-order, linear time-invariant (LTI) system.
The time constant is the main characteristic unit of a first-order LTI system.

## Slide 23: Dynamic Response of Proportional Control
Initially, assume the process is at steady state and the output level equal to the set-point.
At time t = 0, a disturbance is allowed into the process.
If no control action is taken, i.e., output is not altered, the response (controlled variable) will increase.

## Slide 24
The proportional control action brings the level back and maintains it in a certain range near the set-point.
Different responses are obtained depending on the size of the proportional band, PB, of the controller as shown below.

## Slide 27: Linearization
This is a method for assessing the local stability of an equilibrium point of a system of nonlinear differential equations or discrete dynamical systems.
Linearization is an effective method of approximating the response of a function, y = f(x), at any point, p where x = a, based on the value of ‘a’ and slope of the function at x = b,
Given that f(x) is differentiable on [a, b] or [b, a] and that ‘a’ is close to ‘b’, i.e., linearization approximates the output of a function near x = a.

## Slide 29
For any given function, y = f(x), f(x) can be approximated if it is near a known differentiable point.
The basic requirement is that if a function La(x) is a linearization of f(x) at x = a, then La(a) = f(a).
The point-slope form of an equation forms an equation of a line, given a point q is has coordinates (h, k) and slope of the tangent at q is m, then:

## Slide 30
But h = b;
Using point p, where x = a;

## Slide 31
The concept of local linearity applies most to points arbitrarily close to x = a, those relatively very close work relatively very well for linear approximations.
The slope m should be, most accurately, the slope of the tangent at x = a.
The diagram shows tangent line of f(x) at point q.
At point p, f(x+∆x), where ∆x = a –b, is any small positive or negative value, the slope is very nearly of the same magnitude as the tangent line at the point q.

## Slide 32
The final equation for the linearization of a function at x = a, is:
.
The derivative of is and the slope of at ‘a’ is .
Linearization makes it possible to study nonlinear systems and to analyze the behavior or response of a nonlinear function near a given point.

## Slide 33
The linearization of a function is the first order term of its Taylor expansion around the point of interest.
For a system defined by the equation y = f(x); the Taylor expansion at x = a, is:

## Slide 34
The series is truncated to the first order term, i.e.,
This is the content of linearization theorem.
For time-varying systems, the linearization requires additional justification.

## Slide 35: Laplace Transform
Ordinary and partial differential equations describe the way certain quantities vary with time, such as the reaction rate; temperature in heat exchanger; current in an electrical circuit, etc.
These equations are generally attached to initial conditions that describe the state of the system at time, t = 0.

## Slide 36
A very powerful technique for solving these problems is that of the Laplace transform, which transforms the original differential equation into an elementary algebraic expression.
Thee latter can then be simply transformed once again, into the solution of the original problem using Laplace transform method.

## Slide 37
The Laplace transform of a function, f, is defined as:

## Slide 38
F is a complex-valued function of complex numbers; s is the frequency (complex) variable, with units per second; t is the time variable (in sec); st is unit-less.
The parameter s belongs to some domain on the real line or in the complex plane.

## Slide 39
The value of s is chosen appropriately so as to ensure the convergence of the Laplace integral (1).
In a mathematical and technical sense, the domain of s is important.
However, in a practical sense, when solving differential equations the domain of s can be ignored.

## Slide 40
When s is complex number, the notation s = x + iy is used.
The lower case letter denotes signal while capital denotes its Laplace transform, e.g., U denotes L(u), Vin denotes L(vin), etc.
The symbol L is the Laplace transformation symbol, which acts on functions f = f (t) and generates a new function, F(s) = L (f(t)).

## Slide 41: Example-1
1- If f(t) = 1 for t ≥ 0; then:

## Slide 42
2- Let:
i.e.,

## Slide 43
Solution:

## Slide 44
3- Find Laplace transform for f(t) = et:
Solution:
Provided that: , which is true for s > 1

## Slide 45
Compute the Laplace Transforms for the following functions:

## Slide 46: Types of Inputs (Forcing Functions)
A forcing function is a disturbance which is externally applied to a system.
Forcing functions are of considerable importance in theoretical and experimental analysis of control systems.
Response to a forcing function without feed-back is called open-loop response (different from open-loop control).

## Slide 47
Open-loop control is frequently used to describe feed forward control.
The response of a system incorporating feed-back is known as closed-loop response.
The following are common examples of forcing functions: step function; sinusoidal function and pulse function.

## Slide 48
Step
Laplace Transform:
Ramp
Laplace Transform:

## Slide 49
Powers of t:
Impulse
Laplace Transform:
Example:

## Slide 50
Solution
Sine
Laplace Transform:

## Slide 51
Exponential (damp)
Laplace Transform:
Cosine
Laplace Transform:

## Slide 52
Damped ramp
Laplace Transform:

## Slide 53
Damped sine
Laplace Transform:
Damped cosine
Laplace Transform:

## Slide 54
First order differential
Laplace Transform:

## Slide 55: Example-2
Solve:
Using y(0) = 0 and U(s) = 1/s
Solution
Take Laplace Transform:

## Slide 56
Taking inverse Laplace Transforms:
The Laplace transform turned a differential equation into an algebraic equation

## Slide 57
Second order differential
Laplace Transform:
Integral
Laplace Transform:

## Slide 58: Example-3
Use Laplace Transform to solve the differential equation:
Solution:
Laplace Transform:

## Slide 59
Inverse Laplace Transforming:

## Slide 61: Patterns
The time domain is for signals while the frequency domain is their Laplace transforms
Differentiation in one domain correspond to multiplication by the variable in the other domain
Multiplication by an exponential in one domain corresponds to a shift (or delay) in the other